## Slide 1
Development of a GUI Based Control Scheme for Ball-on-Plate System
K Akanksh Pratheek Reddy
Reg. No.: 140907050
Sec. : B , Roll No. : 6
Under The Guidance Of
Dr. K Prabhakar Nayak Mr. Mukund Kumar Menon
Professor Asst. Professor Sr. Scale
Department of ECE Department of ICE
MIT, Manipal MIT, Manipal
Progress Presentation 3
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 2
Department of Electronics and Communication Engineering, MIT, Manipal
Contents
Content | S. Number
Computer Vision – Time Dependency | 3
Controller Simulation | 4
Misc. Progress | 11
Summary | 12
References | 13

## Slide 3
Department of Electronics and Communication Engineering, MIT, Manipal
Computer Vision – Time Dep.
Frame Rate – 30 fps  0.033 sec per frame
Average = 0.36 sec/25 frames  0.014 sec/frame
Sufficient Overhead
Trial No. | Processing Time per 25 frames
1 | 0.36 seconds
2 | 0.40 seconds
3 | 0.42 seconds
4 | 0.32 seconds
5 | 0.40 seconds
6 | 0.36 seconds
7 | 0.36 seconds
8 | 0.38 seconds
9 | 0.32 seconds
10 | 0.34 seconds

## Slide 4
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Mathematical Model – Linearized, Decoupled equations [1]
Open Loop Unstable
Fig. 1 : Control Block Diagram

## Slide 5
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Fig. 2 : Two Poles at Center - Unstable

## Slide 6
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Fig. 3 : Step Response – Highly Unstable

## Slide 7
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
First, Major Controller – Classical PD
Two controllers running independently for each axis
Design Criteria: [2]
Settling Time of less than 5 sec
Overshoot less than 5%
Fig. 4 : Design Criteria - Achieved

## Slide 8
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Fig. 5 : Two Poles in left half plane - Stable

## Slide 9
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Fig. 6 : Step Response – Stable

## Slide 10
Department of Electronics and Communication Engineering, MIT, Manipal
Controller Simulation
Fig. 2 : Trajectory to (120,200) from (0,0)

## Slide 11
Department of Electronics and Communication Engineering, MIT, Manipal
Misc. Progress
Further tuning of Mechanical System
Servo Precision Testing
Accurate mounting of camera
Coordination of Plate/Actuator dynamics and sensing
Rewiring of Power Supply – More Rugged

## Slide 12
Department of Electronics and Communication Engineering, MIT, Manipal
Summary
Mechanical fabrication completed, tuned and Extensively tested
Computer vision algorithm implemented and tested
Mathematical modeling done
PD Controller designed and Simulated
Miscellaneous bridge tasks completed
Implementation of control in Hardware ongoing

## Slide 13
Department of Electronics and Communication Engineering, MIT, Manipal
[1] M. Nokhbeh and D. Khashabi, “Modelling and Control of Ball-Plate System”, Amirkabir Institute of Technology, 2011
[2] A. Kassem, C. Albitar and H. Haddad, “Comparision Between Different Methods of Control of Ball and Plate System with 6DOF Stewart Platform”, in International Federation of Automatic Control, Elsevier, 2015
[3]K. Kyu Lee, G. Btz, and D. Wollherr, “Basketball robot: Ball on-plate with pure haptic information," in IEEE International Conference on Robotics and Automation, May 2008
References